## Slide 1: Understanding and Complying with New Storm Water Mitigation Requirements from the EPA
Qian Liao, Hani Titi, and Jin Li
University of Wisconsin-Milwaukee
WHRP Project 0092-13-03

## Slide 2: Background
U.S. EPA published the new Effluent Limitations Guideline (ELGs) in December 2009
  All construction sites disturbing 20 or more acres of land must sample to stormwater discharge
  The daily average of turbidity must not exceed 280 NTU
  The limitation applies for storms less than a 2-year 24-hour event
The numeric limitation was removed in EPA’s final rule in 2014 as a part of a settlement of industrial law suit. However, EPA may consider additional effluent limitations and monitoring requirement in future regulations.
Little information has been documented for actual turbidity levels in stormwater runoff from Wisconsin construction sites

## Slide 3: Research Activities
Conduct literature review: turbidity, EPA’s ELGs
Take grab samples of stormwater from identified WisDOT construction sites to measure the turbidity, TSS, pH and conductivity
Deploy automated turbidity sampling devices to measure the turbidity time series of the effluent from construction sites.
Explore the correlation between the turbidity runoff and the precipitation
Conduct laboratory experiments to examine the TSS-turbidity correlation

## Slide 4: 1. Literature Review

## Slide 5: Understanding Turbidity
Turbidity is a measure of water clarity, i.e., how much the material suspended in water decreases the passage of light through the water.
Suspended materials mainly include soil particles, algae, microbes and other substances.
Turbidity is an important parameter in assessing the environmental health of water bodies.
Practically, turbidity can be measured by a Nephelometer which detects particle light scattering from the side of the light beam(s) The units of a calibrated nephelometer are called the Nephelometric Turbidity Units (NTU)

## Slide 6: TSS-Turbidity Relation
Total Suspended Solids (TSS): total mass of small solid particles in water which does not settle out by gravity.
TSS is usually measured by filtration, e.g., EPA Standard Method 160.2
Many studies demonstrated good correlations between TSS and turbidity, although correlation coefficients varied significantly, largely due to different properties of solid particles
Better correlations were found for construction site runoff samples, possibly due to the lack of organic matters in soil.
Many studies suggested a linear TSS-Turbidity relation, i.e.,
TSS (mg L-1) = a Turbidity (NTU),
where a = 0.6~3.4 (mg L-1 NTU-1)

## Slide 7: Factors Affect Turbidity Measurements
Factors related samples:
  Particle size, shape, and color
  Water color, dissolved organic matters
Factors related to devices:
  Light sources (e.g., tungsten lamps, LEDs, lasers)
  Type of photodetectors
  Angles of detections
Calibration standards (Formazin or SDVB particles)

## Slide 8: Turbidity of Construction Site Runoff
NCHRP project report (2012)*
* NCHRP (2012) Turbidity reduction and monitoring strategies for highway construction projects. NCHRP Project 25-25(74) Final Report.
Notes: Note: NCHRP: National Cooperative Highway Research Program, (2012)

## Slide 9: 2. Methodology

## Slide 10: Field Grab Sample Collection and Measurement

## Slide 11: Turbidimeters
Lab bench-top nephelometer: HS Scientific DRT-100B turbidimeter
Handheld probe: Turner Designs Cyclops-7 submersible turbidity sensor

## Slide 12: pH and Conductivity
ExTech ExStik EC500 pH/Conductivity handheld sensor

## Slide 13: Total Suspended Solids Measurement
1
2
3
4
Notes: 1. Filter through a Gooch cubicle, 2. Dried in the oven (105 oC) for 1 hour, 3, further dried in the desiccator for 20 min, 4, residuals are weighed.

## Slide 14: Automated Turbidity Sampling Device
Developed based on Turner Designs Cyclops submersible turbidity probes
Measures time series turbidity at major outfalls (streams, storm drains or rivers) of construction sites
Sampling frequency: 17 times a day

## Slide 15: 3. Field Grab Samples

## Slide 16: Identified Sites
Site Name | Location | Grab samples | Automated Samples
A. Kenosha | STH-50 & I-94 | Yes | no
B. Wauwatosa | STH-181 & I-94 | Yes | Yes
C. Racine | SHT-20 & I-94 | Yes | Yes
D. Lake Geneva | STH-50 & US-12 | Yes | Yes
E. Wrightstown | STH-96 & Fox River | No | Yes

## Slide 17: Kenosha Site
Total disturbed land area: 7.7 acres
BMPs: straw mulch, retention pond, ditch checks.
Sampling locations:
  Retention pond
  Inlet of the retention pond
  Paved surface
  Stormwater ditch

## Slide 18: Kenosha Site: Grab Sample Turbidity
Yellow: Oct 5, 2013
Red: Oct 31, 2013

## Slide 19: Wauwatosa Site
Total disturbed land area: 10.9 acres
BMPs: Inlet protections, ripraps, silt fences
Sampling locations:
  Stormwater inlet
  Honey creek

## Slide 20: Wauwatosa Site: Grab Sample Turbidity

## Slide 21: Racine Site
Total disturbed land area: 7.92 acres
BMPs: straw mulch, silt fence, ditch checks
Sampling locations:
  Natural stream along disturbed soil
  Natural stream (outfall)
  Stormwater ditch

## Slide 22: Racine Site: Grab Sample Turbidity
Sampling date: May 30, 2015

## Slide 23: Lake Geneva Site
Total disturbed land area: 11.75 acres
BMPs: silt fence, dewatering pipe and filter bags
Sampling locations:
  Culvert inlets (outfall)
Sampling results: May 30, 2015

## Slide 24: Wrightstown Site
Total disturbed land area: 2.77 acres
BMPs: silt fence, ripraps
No grab samples

## Slide 25: Turbidity Histogram
Turbidity ranged from 20 to 2300 NTU based on 57 Grab samples

## Slide 26: TSS Histogram
44 Samples

## Slide 27: No Correlations among Turbidity, pH and Conductivity

## Slide 28: 4. TSS-Turbidity Relation

## Slide 29: Turbidity of Lab-Simulated Runoff
Laboratory test with soil samples from selected sites to examine
  Characteristics of effluent turbidity time series
  A practical procedure to determine a site specific TSS-turbidity correlation

## Slide 30: Simulated Rainfall-Runoff Turbidity Process
Test 1: Dry soil
Test 2: Wet soil (16 hours after test 1)
A secondary turbidity peak (due to subsurface interflow) can be observed in both tests

## Slide 31: TSS vs. Turbidity: Power Law Relation
Site |  | 
Kenosha | 0.06 | 1.48
Racine | 0.008 | 1.62
Wrightstown | 0.076 | 1.36
Wauwatosa | 0.003 | 1.92
Site |  | 
Kenosha | 0.06 | 1.48
Racine | 0.008 | 1.62
Wrightstown | 0.076 | 1.36
Wauwatosa | 0.003 | 1.92

## Slide 32: or, equivalently,

## Slide 33: 5. Correlation between Turbidity Runoff and Precipitation

## Slide 34: Automated Turbidity Sampling: Sites and Weather Stations
Automated turbidity sampling devices were deployed at four sites:
  Racine (11 events)
  Lake Geneva (8 events)
  Wrightstown (3 events)
  Wauwatosa (8 events)

## Slide 35: Rainfall-Turbidity Runoff Time Series
Example: data series from Lake Geneva Site

## Slide 36: Unit Turbidity Runoff Response Function
Analogous to the unit hydrograph approach, a unit turbidity runoff response function can be reconstructed from recorded turbidity&precipitation time series.
Note: Errors are defined as the ratio of root mean square errors to the peak turbidity level.

## Slide 37: Statistics From Data Series
Total rainfall depth
Average rainfall intensity
Peak rainfall intensity
Event averaged turbidity
Peak turbidity
24-hour averaged turbidity (EPA limitation: <280 NTU)
Turbidity runoff duration
Rainfall centroid time
Turbidity runoff centroid time

## Slide 38: Rainfall-Turbidity Correlation
We claim that statistics of rainfall and turbidity are correlated if
  Linear regression
  And the hypothesis testing rejects the null hypothesis with
Note: √ : correlated, × : uncorrelated
 | Racine | Lake Geneva | Wrightstown | Wauwatosa
Mean turbidity (Ta) vs. mean rain intensity (Ia) | × | × | × | ×
Peak turbidity (Tp) vs. mean rain intensity (Ia) | × | × | × | ×
Mean turbidity (Ta) vs. peak rain intensity (Ip) | × | × | × | √
Peak turbidity (Tp) vs. peak rain intensity (Ip) | × | × | √ | ×
Mean turbidity (Ta) vs. total rain depth (P) | × | × | × | √
Peak turbidity (Tp) vs. total rain depth (P) | √ | √ | √ | √
Peak daily average turbidity (T24) vs. total rain depth (P) | √ | x | √ | √

## Slide 39: Peak Turbidity ~ Precipitation Depth
Good linear relation was found between the peak turbidity and the total precipitation depth for all four sites: , where (NTU/in) for Racine, Lake Geneva, Wrightstown and Wauwatosa sites, respectively

## Slide 40: 24-hour average Turbidity vs. Precipitation Depth
Good linear correlation was found between the maximum 24-hour average turbidity and the total precipitation depth at all but one site

## Slide 41: Conclusions
Turbidity of grab samples during or after storms ranged from 20 to 2,300 NTU, agreed well with the 500~2,000 NTU range reported in NCHRP (2012).
Conventional BMP controls are not able to significantly reduce the turbidity. However, they are effective at reducing soil erosion, runoff volume and speed, thus reducing the total sediment load into receiving waters.
Relation between the TSS and turbidity of grab samples can be described by a power-law relation, i.e., , where the exponent ranged from 1.36 to 1.92, and the coefficient varied significantly from 0.003 to 0.076.
A unit runoff turbidity function, which represents the response of turbidity runoff process to a unit precipitation depth, can be reconstructed from measured data. The reconstructed unit response function was able to reasonably describe all recorded turbidity runoff events.
Both the peak turbidity and the maximum daily average turbidity were found to be linearly correlated with the total precipitation depth for all sampling sites

## Slide 42: Backup Slides

## Slide 43: Turbidity Measurements: Other Methods and Units
Formazin Nephelometric Units (FNU): Since Formazin (a polymer) solution is widely used for calibrating a nephelometer.
Jackson Turbidity Unit (JTU): used for the Jackson Candle method which measures light attenuation as it travels through the column of the sample.
This is no standard method to convert between various turbidity units (e.g., NTU vs. FNU). Note: Turbidity units are NOT physical units
Jackson Candle Method

## Slide 44: EPA Standard Method: 180.1
Based on a comparison of the intensity of light scattered by the sample with that by a standard (Formazin)
Measurement units: NTU
Detecting angle within ±30o of the center
Detector within 10 cm from the light beam
Measurement range: 0~40 NTU. For turbidities exceeding 40 NTU, dilute the sample to <40NTU.

## Slide 45: Turbidimeters
Benchtop meters
  Tungsten lamp
  Superior accuracy and sensitivity
  Complies with EPA standard (EPA Method 180.1)
Handheld meters (field applications)
  Near infrared light source
  Can measure high turbidity (ideal for construction site monitoring)
  Datalogger for automated sampling

## Slide 46: Related Research (Texas DOT)
Performance Testing of Coagulants to Reduce Stormwater Runoff Turbidity (project number: 0-6638)
Objective: to test the polyacrylamide (PAM) as a coagulant for erosion and sediment controls
Findings:
  PAM application on tested clay soils with 1:3 slopes was not effective in reducing runoff turbidity or soil loss
  PAM added in sedimentation devices increased sediment removal rate by 8 to 18 percent, compared with sedimentation without PAM treatment

## Slide 47: Turbidity of Construction Site Runoff
McFalls et al. (2014): Texas DOT project report

## Slide 48: Related Research (Minnesota DOT)
Development and Evaluation of Effective Turbidity Monitoring Methods for Construction Projects (MN/RC 2014-24)
Objective: to investigate turbidity relationships for conditions of Minnesota and to develop protocols for the design and installation of cost-effective monitoring systems.
Findings:
  Relation between turbidity and TSS can be described by a power law with an exponent of 7/5 based on fourteen different soil samples in Minnesota.
  Field monitoring of runoff from construction sites found that turbidity often exceeded 1,000 NTU and sometimes surpassed 3,000 NTU.

## Slide 49: Perkins et al. (2014)
Turbidity-TSS relation for Minnesota soils

## Slide 50: Turbidity Readings: Field Meter vs. Bench-top Turbidimeter
Total field grab samples: 54
For 24 grab samples, turbidity was measured by both the handheld meter onsite and the lab bench-top meter

## Slide 51: pH Histogram
51 Samples

## Slide 52: Conductivity Histogram
49 Samples

## Slide 53: TSS vs. Turbidity: Linear Regression
Site | Coefficient b
Kenosha | 2.16
Racine | 1.04
Wrightstown | 1.15
Wauwatosa | 1.11

## Slide 54: Total Sediment Load
Assume a linear correlation between TSS and turbidity, the total sediment load of an storm event is proportional to , where is the runoff hydrograph.
Assuming that the discharge rises and falls following the same trend as turbidity , the total sediment flux can be estimated to be proportional to

## Slide 55: Total Sediment Load ~ Precipitation Depth
A power law relation is found between and
Site |  | 
Racine |  | 3.27
Lake Geneva |  | 1.25
Wrightstown |  | 1.59
Wauwatosa |  | 1.39
Site |  | 
Racine |  | 3.27
Lake Geneva |  | 1.25
Wrightstown |  | 1.59
Wauwatosa |  | 1.39

## Slide 56: Racine Site Statistics
Event ID | P (in) | Ia (in/hr) | Ip (in/hr) | Ta (NTU) | Tp (NTU) | T24 (NTU) | Dp (hr) | Dt (hr) | Cp (hr) | Ct (hr)
1 | 0.67 | 0.061 | 0.18 | 436 | 1,502 | 662 | 16 | 38 | 10.4 | 16.0
2 | 1.02 | 0.049 | 0.28 | 395 | 2,434 | 727 | 47 | 104 | 17.5 | 40.2
3 | 0.42 | 0.105 | 0.16 | 325 | 936 | 379 | 4 | 10 | 2.9 | 5.5
4 | 0.68 | 0.227 | 0.29 | 227 | 811 | 335 | 4 | 11 | 2.8 | 4.3
5 | 0.80 | 0.400 | 0.77 | 622 | 1,637 | 761 | 2 | 11 | 1.0 | 4.2
6 | 0.90 | 0.450 | 0.86 | 1,077 | 1,767 | 1,077 | 2 | 16 | 1.0 | 7.2
7 | 0.61 | 0/153 | 0.42 | 166 | 511 | 235 | 5 | 16 | 1.6 | 6.8
8 | 0.25 | 0.125 | 0.14 | 142 | 362 | 246 | 2 | 14 | 1.6 | 6.1
9 | 0.37 | 0.123 | 0.32 | 122 | 238 | 152 | 3 | 21 | 2.0 | 10.4
10 | 0.36 | 0.120 | 0.26 | 67 | 185 | 98 | 4 | 21 | 1.9 | 9.6
11 | 0.34 | 0.068 | 0.12 | 91 | 462 | 225 | 5 | 24 | 3.0 | 8.6

## Slide 57: Lake Geneva Site Statistics
Event ID | P (in) | Ia (in/hr) | Ip (in/hr) | Ta (NTU) | Tp (NTU) | T24 (NTU) | Dp (hr) | Dt (hr) | Cp (hr) | Ct (hr)
1 | 1.13 | 0.094 | 0.36 | 433 | 1.747 | 594 | 23 | 38 | 10.8 | 13.4
2 | 0.35 | 0.088 | 0.27 | 198 | 1,130 | 541 | 15 | 21 | 3.1 | 7.0
3 | 1.03 | 0.515 | 0.61 | 671 | 2,390 | 1,108 | 2 | 27 | 1.4 | 9.3
4 | 0.26 | 0.065 | 0.09 | 236 | 728 | 316 | 16 | 32 | 9.1 | 18.0
5 | 0.51 | 0.510 | 0.51 | 227 | 1,215 | 382 | 2 | 27 | 1.0 | 10.5
6 | 1.15 | 0.383 | 0.99 | 623 | 2,468 | 1,034 | 3 | 24 | 1.9 | 10.3
7 | 1.30 | 0.650 | 1.17 | 534 | 1,978 | 884 | 2 | 17 | 1.9 | 8.0
8 | 0.83 | 0.415 | 0.51 | 1,138 | 1,636 | 1,065 | 2 | 14 | 1.4 | 4.4

## Slide 58: Wrightstown Site Statistics
Event ID | P (in) | Ia (in/hr) | Ip (in/hr) | Ta (NTU) | Tp (NTU) | T24 (NTU) | Dp (hr) | Dt (hr) | Cp (hr) | Ct (hr)
1 | 1.41 | 0.282 | 0.64 | 767 | 1,343 | 880 | 5 | 12 | 2.6 | 4.1
2 | 2.50 | 0.417 | 0.96 | 1,975 | 2,500 | 1,975 | 6 | 7 | 2.2 | 3.3
3 | 0.75 | 0.150 | 0.44 | 736 | 1,009 | 736 | 5 | 7 | 3.2 | 3.3
Wauwatosa Site Statistics
Event ID | P (in) | Ia (in/hr) | Ip (in/hr) | Ta (NTU) | Tp (NTU) | T24 (NTU) | Dp (hr) | Dt (hr) | Cp (hr) | Ct (hr)
1 | 0.41 | 0.137 | 0.29 | 41 | 133 | 58 | 3 | 16 | 1.4 | 7.4
2 | 0.90 | 0.225 | 0.58 | 125 | 463 | 171 | 4 | 13 | 1.5 | 5.7
3 | 0.17 | 0.057 | 0.08 | 21 | 64 | 36 | 3 | 14 | 1.9 | 5.8
4 | 0.15 | 0.050 | 0.06 | 32 | 103 | 43 | 3 | 13 | 2.2 | 6.5
5 | 0.55 | 0.275 | 0.50 | 86 | 180 | 79 | 2 | 10 | 1.1 | 3.9
6 | 0.30 | 0.150 | 0.22 | 44 | 113 | 49 | 2 | 13 | 1.7 | 6.8
7 | 0.27 | 0.054 | 0.09 | 42 | 153 | 48 | 5 | 13 | 3.4 | 6.2
8 | 0.15 | 0.025 | 0.04 | 35 | 112 | 39 | 7 | 18 | 3.3 | 8.3