# Asphalt Panels, Item SPV.0180.xx.

A  Description

This special provision describes furnishing and placing asphalt protection in accordance with Chapter 29, Part 2 of the American Railway Engineering and Maintenance-of-Way Association (AREMA) Manual, as shown on the plans, and as hereinafter provided.

B  Materials

Shop drawings and data on the material and its installation, including joint details, shall be submitted to the engineer for approval.

B.1  Asphalt Panels

Use two layers of asphalt panels, each ½-inch thick, in accordance with Chapter 29, Part 2.4.3.  Use 4-foot by 8-foot sections, or as approved by the Engineer.

B.2  Adhesive

Use adhesive for bonding the asphalt panels to the butyl rubber membrane in accordance with Chapter 29, Part 2.3.6.

B.3  Sealing Compound for Joints

Use a sealing compound that is compatible with both the membrane and the asphalt panels, in accordance with Chapter 29, Part 2.5.  Submit to the engineer for approval appropriate literature and samples of the sealing compound to be furnished.

C  Construction

Place the asphalt protection in accordance with Chapter 29, Parts 2.8.4.1, 2.8.4.4 and 2.8.4.5, and as hereinafter provided.

C.1  Asphalt Panels

Place the asphalt panels dry (without bonding adhesive) on the horizontal surface of the steel deck.  Place the asphalt panels on the inclined or vertical surfaces using a coating of bonding adhesive.

C.2  Joints

Stagger joints between the asphalt panel layers such that no joint in the second layer is within 6 inches of a joint in the first layer.  Lay all joints tight and seal them with an approved sealing compound as recommended by the sealant manufacturer.

D  Measurement

The department will measure Asphalt Panels by the square yard acceptably completed.

E  Payment

The department will pay for the measured quantity at the contract unit price under the following bid item:

| ITEM NUMBER | DESCRIPTION | UNIT |
| --- | --- | --- |
| SPV.0180.xx | Asphalt Panels | SY |

Payment is full compensation for furnishing and placing asphalt panels, bonding adhesive and sealing compound; and for furnishing all labor, tools, equipment, materials, and incidentals necessary to complete the work.

05/07