# Bearing Repair, Item SPV.0060.XX.

A  Description

This special provision describes removing the bearings at the piers, blast cleaning and priming the bearings, furnishing and placing shims, resetting the bearings, and furnishing and placing new anchor bolts. All work shall be in accordance with the pertinent provisions of the standard specifications, the plans, and as hereinafter provided.

B  (Vacant)

C  Construction

Clean the bearings to a near white finish. Prime the bearings with one coat of organic zinc primer.

D  Measurement

The department will measure Bearing Repair as each individual bearing acceptably completed.

E  Payment

The department will pay for the measured quantity at the contract unit price under the following bid item:

| ITEM NUMBER | DESCRIPTION | UNIT |
| --- | --- | --- |
| SPV.0060.xx | Bearing Repair | Each |

Payment is full compensation for removing, cleaning, painting, and resetting bearings; furnishing, painting, and placing shim plates and anchor bolts; and for furnishing all labor, tools, equipment, materials, and incidentals necessary to complete the contract work.

07/05