# Combination Railing, Item SPV.0090.XX.

A  Description

This special provision describes furnishing and erecting a pedestrian railing fabricated from structural steel and glue laminated timber in accordance with the requirements of sections 513 and 507 of the standard specifications, as shown on the plans, directed by the engineer, and as hereinafter provided.

B  Materials

Modify subsection 507.2.3 as follows: Only Chromated Copper Arsenate (CCA), Ammoniacal Copper Arsenate (ACA), and Ammoniacal Copper Zinc Arsenate (ACZA) will be allowed.

C  (Vacant)

D  Measurement

The department will measure Combination Railing by the linear foot acceptably completed.

E  Payment

The department will pay for the measured quantity at the contract unit price under the following bid item:

| ITEM NUMBER | DESCRIPTION | UNIT |
| --- | --- | --- |
| SPV.0090.xx | Combination Railing | LF |

Payment is full compensation for furnishing, framing, fabricating, delivering and erecting the railing; treating the railing; furnishing and placing metal shims under the bases, if required; furnishing and placing the anchor bolts; and for furnishing all labor, tools, equipment, materials, and incidentals necessary to complete the contract work.

07/05