## Slide 1: Traffic Control Devices
Drums
42” Cones
Barricades
Arrow Boards
Portable Changeable Message Boards
Signs and Sign Stands
Truck/Trailer Mounted Attenuators
Pedestrian Accommodations
Smart Work Zones
Notes: May want to include a plug for our work zone devices purchasing contract

## Slide 2: MASH Requirements
Manual for Assessing Safety Hardware (MASH) 2016
  All devices manufactured after December 31, 2019 must successfully pass MASH 16
NCHRP Report 350 & MASH 09
  Devices may still be used throughout their normal service lives, WisDOT has set sunset dates in agreement with other states in the Midwest
Notes: https://safety.fhwa.dot.gov/roadway_dept/countermeasures/reduce_crash_severity/docs/memo_joint_implementation_agmt.pdf

## Slide 3: WisDOT Approved Products List (APL)
Set up to help inspectors
If you want a device added contact: DOTSignMarkWZMaterials@dot.wi.gov
Sunset dates for certain devices shown

## Slide 4: Quality Standards
Acceptable

## Slide 5: Quality Standards
Marginal

## Slide 6: Quality Standards
Unacceptable

## Slide 7: Traffic Control Drums
Spec. 643, SDD 15c11b
Large target value
4”-6” white and fluorescent orange sheeting
Weighted base
Clean/not crushed
Brown Co. 7/18/2019

## Slide 8: 42-Inch Cones
Spec. 643, SDD 15c11b
Smaller target value
4”-6” white and fluorescent orange sheeting
Weighted base
½ the spacing of drums
Do not use in tapers
Washington Co. 11/25/2019

## Slide 9: Drums vs. Cones
Dane Co. 8/7/2019

## Slide 10: Barricades
Spec. 643, SDD 15c11b
Three panels with orange and white stripes
Stripes point down toward traffic
Barricades at night need lights
Iron Co. 8/20/2019

## Slide 11: Signs
Spec. 643
Fluorescent Orange
  Use APL
Diamond are typically 48”x48”
Roll-up or metal
Stands must be crashworthy
200 ft. minimum spacing
Utility 7/18/2019
Notes: Use Road Work 1 mile on Freeways and Expressways

## Slide 12: Correct Advance Warning Sign
Road Work Ahead vs. Road Work 1 Mile
Iowa Co. 8/6/2019
Barron Co. 7/9/2019

## Slide 13: Portable Changeable Message Signs (PCMS)
Spec. 643, TEOpS 6-02
Letter height, trailers 18”, vehicles 10”
Three lines of text
Two phases
  Problem/Action
Do not use words Danger, Hazardous, and Caution
Mounting height, 5 ft. rural, 7 ft. urban
Lincoln Co. 8/20/2019

## Slide 14: Arrow Boards
Spec. 643
Only use Flashing Arrow
Do not use chevrons
Only use arrow for lane closure
Solid bar or 4 corners for shoulder closures or boards within a lane closure
Any lights out in the head of the arrow is unacceptable
Improvement Project 7/15/2019

## Slide 15: Truck/Trailer Mounted Attenuators
HMM 5-1-43
Anytime vehicles are used as a protection vehicle for workers
Use the proper TMA for the facility
Have the proper weight for the host vehicle
Use manufacturers roll ahead distance

## Slide 16: Truck/Trailer Mounted Attenuators
Crashworthiness
If you have NCHRP 350 TL-3 TMA’s
  Use until end of useful life or sunset date
When purchasing new TMA’
  MASH TL-3
Photo: TrafFix Devices Scorpion II
Notes: https://www.youtube.com/watch?v=OdIYXnYWEfM
https://www.youtube.com/watch?v=ce0B8jyvE9o

## Slide 17
Truck/Trailer Mounted Attenuators

## Slide 18: Temporary Signals
Spec. 661
Two signal heads required
Stop bar required
Traffic dependent
Electrical APL

## Slide 19: Pedestrian Accommodations
Detour pedestrians around work
  Do not close off both side of sidewalk if available
Stop work allow them to pass through
Improvement Project 11/18/2019

## Slide 20: Smart Work Zones
New devices
Smart Arrow Boards
Queue Warning Systems
Start and End of Work Zone tracking: iPin, sensors
Photo: Street Smart Rentals

## Slide 21: High Visibility Apparel
HMM 05-02-10
Daytime
  Class 2 or Class 3
Nighttime
  Vest and Pants Required
ANSI 107-2015 Type R
Clean
Photo: HiVis Supply

## Slide 22: Flagging
2020 Flagging Handbook
Flaggers must be certified for work on the state highway system
Vest and pants
  Minimum Class 2 Vest
  Class E pants
Proper sign size and staff height

## Slide 23: Temporary Portable Rumble Strips
Flagging Handbook, SDD 15c12, Spec 104.6
1 hour or more
Only use TPRS from APL
40 mph and above
Spacing of strips depends on speed
Monitor hourly for placement
Notes: make note of change for this year, all flagging operations require them and only one set in each direction